# Carriage Stabilization — Simulation Refactor Spec
## Objective
Delete plot_time_series_cmd.py and rebuild the simulation stack for clarity and testability. The new system simulates a motorized carriage traveling on the outer rim of a fixed wheel, with feedback from the FLC’s motor_cmd. It outputs realistic IMU-like raw signals and a clean plot script.
## Artifacts to (Re)Create
1. simulation.py — physics + IMU synthesis (no plotting, no CLI).
2. mock_spi.py — thin adapter exposing imu_read() by delegating to simulation.py.
3. plot_simulation.py — plotting only (θ, ω, motor_cmd vs time). No simulation logic, no argparse.
4. sim_config.toml — simulation parameters/constants.
5. flc_config.toml — FLC parameters only (membership functions, rule base, scaling). Keep existing content, remove simulation-related items.
## Config Separation
### 1) flc_config.toml (FLC-only)
- Contents:
  - [flc_scaling] (e.g., THETA_SCALE_FACTOR, OMEGA_SCALE_FACTOR)
  - [membership_functions.theta], [membership_functions.omega]
  - [[rule_base]] blocks (theta_coeff, omega_coeff, bias)
- Keep controller-side items that truly belong to the FLC pipeline (e.g., TARGET_HZ only if your controller loop timing depends on it).
- Remove simulation/system items (wheel radius, mass, torque/force, initial angle, IMU noise, etc.) and relocate them to sim_config.toml.
- Current reference file (to update accordingly).
### 2) sim_config.toml (new; simulation-only)
Suggested schema:
[simulation.timing]
SAMPLE_RATE_HZ = 50.0 # dt = 1 / SAMPLE_RATE_HZ
DURATION_S = 10.0 # total simulated seconds

[simulation.initial_conditions]
THETA_INITIAL_RAD = 0.0 # initial angle (rad)
OMEGA_INITIAL_RAD_S = 0.0 # initial angular rate (rad/s)

[simulation.mechanics]
WHEEL_RADIUS_M = 0.604 # 604 mm -> meters
CARRIAGE_MASS_KG = 0.80 # or from prior estimate; adjust as needed
MOTOR_FORCE_N = 8.71 # max tangential force at rim for motor_cmd=±1
GRAVITY_M_S2 = 9.80665 # g

[simulation.imu_model]
GYRO_FS_RAD_S = 4.363 # gyro full-scale in rad/s (maps to ±16384 raw)
ACCEL_RAW_FS = 16384 # raw full-scale counts for accel mapping
NOISE_SPAN = 3 # randint(-NOISE_SPAN, +NOISE_SPAN) added to x_raw, y_raw

[logging]
LEVEL = "INFO"
## Simulation Model (in simulation.py)
- The simulator advances one fixed timestep dt = 1 / SAMPLE_RATE_HZ.
- Controller computes motor_cmd ∈ [-1, +1] each step (FLC external).
- Dynamics (simple, requested form):
  - alpha = (MOTOR_FORCE_N * motor_cmd) / CARRIAGE_MASS_KG + GRAVITY_M_S2 * sin(theta)
  - omega ← omega + alpha * dt
  - theta ← theta + omega * dt
- IMU synthesis:
  - x_raw = int(ACCEL_RAW_FS * sin(theta)) + randint(-NOISE_SPAN, +NOISE_SPAN)
  - y_raw = int(ACCEL_RAW_FS * cos(theta)) + randint(-NOISE_SPAN, +NOISE_SPAN)
  - omega_norm = clamp(omega / GYRO_FS_RAD_S, -1, +1)
  - omega_raw = int(ACCEL_RAW_FS * omega_norm) (reuse ±16384 scale for 16-bit alignment)
  - Clamp all raw outputs to ±16384.
- No legacy “modes” (e.g., OMEGA_MODE)—they’re removed.
## mock_spi.py (adapter only)
- Provide imu_read() returning 6 bytes [xL,xH, yL,yH, omegaL,omegaH].
- Internally hold a CarriageSimulator instance from simulation.py.
- Read most-recent motor_cmd from a small mailbox (e.g., set_motor_cmd(u) setter called by the caller) before stepping the sim.
- No slope ramps, no synthetic step trig—all kinematics come from the simulator.
- Keep code short and obvious.
## plot_simulation.py (plot only; no argparse)
- Imports both configs:
  - Loads FLC via flc_config.toml (for the controller object only).
  - Loads SIM via sim_config.toml (to build the simulator).
- Runs a loop for DURATION_S * SAMPLE_RATE_HZ steps:
  - Read last (x_raw, y_raw, omega_raw) from mock_spi.imu_read().
  - Convert to normalized theta_norm, omega_norm exactly as your runtime does.
  - Compute motor_cmd = flc.calculate_motor_cmd(theta_norm, omega_norm).
  - Call mock_spi.set_motor_cmd(motor_cmd) for the next step.
  - Log arrays of t, theta, omega, motor_cmd for plotting.
- Plot θ, ω, and motor_cmd vs time using the same axis conventions you had before (shared time axis, clean labels, grid, dashed zero-lines). No command-line arguments—everything comes from the two TOML files.
## Migration Notes (from current flc_config.toml)
Move these out of FLC config into sim_config.toml:
- Wheel/drive geometry, mass/force, gravity, initial θ, IMU noise span, gyro FS (if treated as sensor model).
- Keep in FLC config: scaling factors, membership functions, and rule base (plus any FLC-only runtime constants). See current entries to relocate (e.g., CARRIAGE_MASS, MOTOR_TORQUE, THETA_INITIAL, NOISE_SPAN, possibly GYRO_FULL_SCALE_RADS_S).
## Non-Goals / Removed
- Delete plot_time_series_cmd.py.
- Remove argparse usage entirely.
- Remove legacy OMEGA_MODE, slope ramps, base offsets, and other ad-hoc synthesis.
## Acceptance Criteria
- Clean module boundaries:
  - Physics in simulation.py
  - Device adapter in mock_spi.py
  - Visualization in plot_simulation.py
- End-to-end closed loop runs with only the two TOML files.
- Plots show responsive negative feedback (θ and ω stabilize/track reasonable behavior when FLC scaling is sane).
- Code is concise, readable, and well-commented; no dead paths or legacy flags.